## Slide 1: S2 Geometric Calibration
Sentinel-2 Geometric Calibration
S. Clerc (ARGANS) and the MPC Team
Sioux Falls, 13 November 2017

## Slide 2: Sentinel 2 Geometry: definitions
Sentinel 2 Geometry: definitions
Main Sentinel 2 products:
  Level 1B: radiances, in sensor geometry: not publicly disseminated
  Level 1C: TOA reflectances in cartographic projection (UTM – MGRS)
  Level 2A: BOA reflectances – same projection: currently produced systematically over Europe only
Definitions
  MSI detector = OLI module
  MSI pixel = OLI detector
  GRI (Global Reference Image): set of reference images used for geometric refinement
  Sentinel 2 Tile or L1C Granule: a 110 x 110 km tile based on the MGRS tiling
Notes: Could be moved to Ferran’s part

## Slide 3: Sentinel 2 Geometric Accuracy Requirements
Sentinel 2 Geometric Accuracy Requirements
Geometric requirement justification
  Sentinel 2 is designed to produce high revisit time series at medium resolution
  Geometric requirements ensure the repeatability of images
  And contribute to image quality (multi-spectral registration)
Notes: To be reviewed by Airbus
Illustration of Sentinel 2 hardware (me)

## Slide 4: Sentinel 2 Geometric Accuracy Requirements
Sentinel 2 Geometric Accuracy Requirements
Design considerations
  MSI Instrument with SiC structure ensures very good thermo-elastic stability
  Sentinel 2 has a high-performance Attitude and Orbit Control System
    High-precision fibre optics gyro
    Multi-head star tracker, mounted on instrument - 2 / 3 heads cold redundancy
    Gyro-stellar estimator
    2-band GNSS receiver
  Geometric refinement with a Global Reference Image to reach multi-temporal registration performance
Global Reference Image
Notes: To be reviewed by Airbus
Illustration of Sentinel 2 hardware (me)

## Slide 5: Sentinel 2 Geometric Accuracy Requirements
Sentinel 2 Geometric Accuracy Requirements
Absolute geolocation
  Without GCP (current processing baseline):
    < 20 m at level 1B (i.e. in sensor geometry)
  With GCP (geometric refinement - activation planned in 2018)
    < 12.5 m at level 1C (cartographic projection)
  Measurement methodology
    B04 (Red) is the reference band for geolocation measurements
    At tile level: average error over all GCPs
    Mission performance: 95% value of all tiles
Notes: To be checked by Thales
Illustration of the verification method (Thales)

## Slide 6: Sentinel 2 Geometric Accuracy Requirements
Sentinel 2 Geometric Accuracy Requirements
Multi-temporal (relative) geolocation
  Without GCP (current processing baseline):
    No specification, but performance continuously monitored
  With GCP (geometric refinement - activation planned in 2018)
    < 3 m at Level 1C
  Measurement methodology
    B04 (Red) is the reference band for geolocation measurements
    Using a pair of recent images of the same tile, for the same repeat orbit
    At tile level: 95.5% percentile Circular Error over all control points
    Mission performance: 95% value for all tiles
Notes: Idem slide 4

## Slide 7: Sentinel 2 Geometric Accuracy Requirements
Sentinel 2 Geometric Accuracy Requirements
Multi-spectral registration
  For any pair of spectral bands, < 0.3 of the coarser pixel size
  At Level 1B
  Measurement methodology
    Performance measured for textured, cloud-free images
    Measurements done for a set of band pairs – results depend on correlation performance (landscape dependent). Measurement at L1B Measurements more difficult for B10 (cirrus band)
    99.7% percentile Circular Error over all control points
Notes: Idem Slide 4

## Slide 8: Sentinel 2 Geometric Calibration Approach
Sentinel 2 Geometric Calibration Approach
Relative line of sight calibration:
  A set of Roll, Pitch, Yaw biases (actual to reference viewing frame)
    Adjusted regularly in the first year after launch
  A time-lag (actual to on-board time reference)
    Characterized during commissioning phase
How?
  Acquisition on a small sites very well localized
  Compute the localization error
  Find the 3 correction angles minimizing rms error
Notes: To be reviewed by Airbus (CNES ?)

## Slide 9: Sentinel 2 Geometric Calibration Approach
Sentinel 2 Geometric Calibration Approach
Spacecraft model bias calibration coefficients:
  Relative Line-of-Sights for each pixel of each detector and each band
  Corrects optical distortions and aberrations
    Characterized during commissioning phase
How?
  Acquisition on a large site covering the full swath equipped with GCPs
  Estimation and correction of all biases
Notes: To be reviewed by Airbus (CNES ?)

## Slide 10: Sentinel 2 Geometric Calibration Approach
Sentinel 2 Geometric Calibration Approach
The Global Reference Image
  Each data-strip is co-registered with images from the GRI, in order to refine the viewing model
    On GRI for the whole mission (TBC), elaboration in progress
    Same GRI for S2A and S2B
The Digital Elevation Model
  The DEM contributes to the geolocation error budget in mountainous areas
  Current DEM is Planet DEM (90 m horizontal resolution)
Notes: To be reviewed by Airbus

## Slide 11: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
The viewing biases evolve slowly during the first year in orbit
  Slow stabilization for yaw bias for S2A and S2B
  Slow stabilization for S2B pitch angle
Small orbital trend for the pitch angle
  Latitude dependence of the pitch bias, due to Star Tracker thermo-elastic deformations
  Amplitude changes seasonally
  This orbital effect will be cancelled after activation of the GRI
  Pitch Bias calibrated for 20° N latitude to account for the North/South emerged land imbalance.
Notes: To be reviewed by Airbus (CNES) and Thales
Illustration of evolution of R,P,Y (me or Thales)
latitude dependence of pitch (Thales)

## Slide 12: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Spectral co-registration
  Biases are very stable over time, confirming the excellent instrument stability
  Main contributor: disturbances from rotating solar panel
    Oscillations uncontrolled by accurately measured by AOCS
    Reduced on S2B (vs S2A) thanks to design improvement
Oscillations due to control error
Filtering of AOCS measurements
Notes: To be reviewed by Airbus / Thales

## Slide 13: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Global Reference Image 1/2
  Nominal GRI completed
    Validation in progress
    Accuracy of the GRI so far is in line with expectations
  Extension to small islands and Northern latitudes (Greenland – Siberia) in progress
    If no reference Ground Control Points are available, the GRI is built on a “best-effort” basis: still ensures the fulfilment of multi-temporal performance
  Geometrical refinement algorithm is currently tested and fine-tuned
    Improve robustness before activating systematic production
Notes: To be reviewed by IGN / Airbus
Illustration of GRI coverage and/or performance validation (IGN)

## Slide 14: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Global Reference Image 2/2
  After activation, a reprocessing campaign of the 2015-2018 archive is planned
  Users have requested a “product” version of the GRI: global set of L1C products with optimal geolocation => in progress
  Long-term evolution of the GRI, under discussion:
    Evolution of the landscape ?
    Winter/summer GRI ?
    Collaborative GRI (with contributed ground control points) ?
Original image
Notes: To be reviewed by IGN / Airbus / CS (Sébastien Harasse)
Illustration of the converted L1C GRI ? (CS)

## Slide 15: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Global Reference Image 2/2
  After activation, a reprocessing campaign of the 2015-2018 archive is planned
  Users have requested a “product” version of the GRI: global set of L1C products with optimal geolocation => in progress
  Long-term evolution of the GRI, under discussion:
    Evolution of the landscape ?
    Winter/summer GRI ?
    Collaborative GRI (with contributed ground control points) ?
Reference image
Notes: To be reviewed by IGN / Airbus / CS (Sébastien Harasse)
Illustration of the converted L1C GRI ? (CS)

## Slide 16: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Digital Elevation Model
  Some quality issues found in mountainous areas, leading to significant geolocation errors locally
  DEM accuracy not uniform, especially at high latitudes
  Evaluation of a new DEM for the Copernicus programme in progress
  Some users would like to create customized products with a proprietary DEM
    On-demand processing service ?
DEM 1 DEM 2 DEM3 DEM4 DEM5 DEM6
Notes: To be reviewed by IGN

## Slide 17: Sentinel 2 Geometric Calibration Experience
Sentinel 2 Geometric Calibration Experience
Anomalies
  On-board anomalies have led to temporary degradation of the geolocation performance at the beginning of the mission
  Most recent one due to a sub-optimal alignment of the redundant Star Tracker head (August 2016)
  No anomaly impacting geometric performance since then
  Geometric performance is continuously monitored in real time for S2A and S2B
Notes: Illustration s2check plots (me)

## Slide 18: Sentinel 2 Geometric Performances
Sentinel 2 Geometric Performances
Absolute Geolocation
  Current best estimate: S2A: 10.5 m – S2B: 11.1 m
  Performance computed over a sliding window
Geometric calibrations
S2A
S2B
Notes: TBW Thales

## Slide 19: Sentinel 2 Geometric Performances
Sentinel 2 Geometric Performances
Multi-temporal Geolocation
  Current best estimate: S2A: 11. 5 m – S2B: 13.8 m
  Histogram of co-registration performance (in pixels at 99.7%)
S2A
S2B
Notes: TBW Thales

## Slide 20: Sentinel 2 Geometric Performances
Sentinel 2 Geometric Performances
Multi-spectral co-registration
  Measured worst-cases among band couple: S2A: 0.21 pixels – S2B: 0.18 pixels at 99.7%
  Example for visible bands (B02/B04)
S2A
S2B
Notes: TBW Thales

## Slide 21: Sentinel 2 Geometric Calibration
Sentinel 2 Geometric Calibration
How to facilitate the combined use of Sentinel 2 and Landsat ?
  Use common conventions to define geometric performance
  Use of a common projection system (cf. HLS project)
  Use of a common Global Reference Image
  Use of a common DEM
  Systematic monitoring of co-registration performance
Notes: To be reviewed by Airbus