## Slide 1: S2 Cal/Val Overview
Sentinel-2 Cal/Val Overview
Ferran Gascon on behalf of Sentinel-2 Data Quality Team
Sioux Falls, 13 November 2017

## Slide 2: Outline
Band 11
B11
Sentinel-2 Cal/Val Overview (Ferran Gascon)
Sentinel-2 Radiometry Cal/Val (Bruno Lafrance)
Sentinel-2 Geometry Cal/Val (Sébastien Clerc)

## Slide 3: Mission Status / Highlights
Band 11
B11
Both Sentinel-2A and -2B operational.
Systematic coverage of Europe, Greenland and Africa every 5 days, and rest of the World every 10 days.
Surface reflectance product (Level-2A) over Europe distributed since 2nd May 2017.
Completed reprocessing of Sentinel-2A commissioning phase products.
All products available through Copernicus Open Access Hub:
  http://scihub.copernicus.eu

## Slide 4: Mission Status / Revisit

## Slide 5: Mission Status / Surface Reflectance
Notes: The Sen2Cor processor (version 2.4.0) is generating bottom-of-atmosphere (BOA) reflectance products.
It generates daily up to 300GB of L2A products (~600 Tiles per Day).
L2A products are made available as from 02 May 2017 through http://scihub.esa.int
Products granularity of L2A is the same as L1C available on SciHub.

## Slide 6: Mission Status / Next Steps
Band 11
B11
Q4 2017: Global 5-day revisit using 4th ground station (Inuvik, Canada) and/or EDRS (European Data Relay System).
29-31 January 2018: 2nd Sentinel-2 Validation Team Meeting.
2018: Completion of the conversion of Sentinel-2 archive into new tile format.
2018: Operational Level-2A global production.
2019: Start reprocessing of all archived data (~5PB) with geometry-refining (using GRI) and operational L2A processor.

## Slide 7: Data Quality / Products Evolution
Band 11
B11
October 2017: New Processing Baseline 02.06 since end of October. Change of naming convention (product discriminator).
2018: Start of the geometry-refined production using GRI (Global Reference Image) to reach multi-temporal registration of 0.3 pixels CE95.
2018: Usage of better DEM to improve geolocation over mountainous regions.
2018: Masks in raster format.
Under assessment: Offset on reflectances.

## Slide 8: Data Quality / Last Year Events
S2A Routine Operations
S2A 02.04
15 Jun 17
7 Mar 17
S2B Launch
S2A 02.05
19 Apr 17
S2B 02.05
30 May 17
Decontamination
Jan 2017
S2B Commissioning
Decontamination
May 2017
S2B Routine Ops
S2B 01.01
6 Dec 16
Compact
naming
S2B 02.06
S2A 02.06
23 Oct 17
Decontamination
Nov 2017
Decontamination
Jul 2017

## Slide 9: Data Quality / L1C Product Performances
Band 11
B11
Next two presentations...

## Slide 10: Data Quality / The Team
Team in charge of all aspects related to data quality (including algorihtms and products evolution, cal/val and quality control)
S2 MPC (Mission Performance Centre)
Ferran Gascon (ESA)
Enrico Cadau (ESA)
Roberto De Bonis (ESA)
Laëtitia Pessiot (CSSI)
Sébastien Clerc (ACRI-ST)
Catherine Bouzinac (CSSI)
Dimitra Touli-Lebreton (ADS)
Bruno Lafrance (CSSI)
Stéphane Massera (IGN)
Marion Neveu (TAS)
Aude Espesset (TAS)
Bahjat Alhammoud (ARGANS)
Sébastien Harasse (CSSI)
Jan Jackson (ARGANS)
Dimitra Tzigkari (ARGANS)
Alejandro García-Soto (DEIMOS)
David Ros (ACRI-ST)
Françoise Viallefont (ONERA)
Jérôme Louis (Telespazio)
Vincent Debaecker (Telespazio F)
Bringfried Pflug (DLR)
Magdalena Main-Knorn (DLR)
Uwe Müller-Wilm (Telespazio D)
Vincent Lonjou (CNES)
Florie Languille (CNES)
Angélique Gaudel-Vacaresse (CNES)
Jean-Louis Raynaud (CNES)
Emmanuel Lourme (CNES)

## Slide 11: S2 image of a glacier
http://sentinels.copernicus.eu