## Slide 1: Sentinel-2 Radiometry Cal/Val
Sentinel-2 Radiometry Cal/Val
Bruno Lafrance with contributions from MPC Team
Bahjat Alhammoud
Dimitra Touli Lebreton
and from Vincent Lonjou (CNES)
ECCOE, Sioux Falls, 2017 Nov. 13th & 14th

## Slide 2: S2 Radiometric calibration
How is performed the radiometric calibration of S2 MSI
  Nominal calibration performed by using the on-board sun-diffuser  Absolute gain monitoring per band  Relative gains monitoring (inter-detector pixel variations per detector module and band)
  A validation is performed using vicarious methods
  Mission requirements: the absolute radiometric uncertainty shall be better than 5% (target 3%)

## Slide 3: S2 Radiometric calibration
Nominal estimate of absolute gains based on sun-diffuser acquisitions
Measurements corrected with:
Dark correction + relative gain correction
(non-linearity and non-uniformity corrections)
Simulation
Average over valid detector pixels
for each band b
Stray-light perturbation
Sun-diffuser BRDF
Solar irradiance
Average ratio of detector pixel measurements over simulations

## Slide 4: S2 Radiometric calibration
Sun-diffuser Bidirectional Reflection Distribution Function characterization
  On-ground test bench measurements  sun-diffusers’ reflectance for each detector pixel (per band and detector module) for a set of different illumination angles and different viewing angles
  First version of the BRDF characterization
    Interpolations to define the BRDF per detector pixel
    Fixed viewing angle per detector pixel
    Nodes of illumination angles (SZA, SAA)
  Refined version of the BRDF
    Fitting a BRDF Rahman angular model
SZA (°): 59.5 61.0 62.5
SAA (°): 15 20 25 30 35

## Slide 5: S2 Radiometric calibration
S2B absolute calibration : use of the initial sun-diffuser BRDF
Decontamination
(May 3rd 2017)
Date
VNIR absolute gains stable since Mid-April in a range of ±0.2%
B01 and B08 bands: variations up to 0.75% since first calibration
Not a real change of the sensor sensitivity
Variations due to a limitation of the sun-diffuser BRDF accuracy
Time variation of the SWIR band sensitivity is properly monitored
Decontamination allows retrieving the initial sensitivity level of SWIR bands and reduces the slopes of decrease with time

## Slide 6: S2 Radiometric calibration
S2B absolute calibration : improvements by using a refined sun-diffuser BRDF model
Great improvement of the stability for the absolute gains estimate
Temporal evolution of absolute gains for SWIR bands becomes smoother
Changes for the first acquisition (ref)
Operationally applied since 2017 October 23rd
(older products will be reprocessed)
A very good stability
Decontamination
(May 3rd 2017)
Date

## Slide 7: S2 Radiometric calibration
S2A absolute calibration : use of the initial sun-diffuser BRDF
    A trend of sensitivity loss seems to be engaged for VNIR band
    -0.6% to -0.9% depending on the band
Change of Earth-Sun distance calculation

## Slide 8: S2 Radiometric calibration
S2A absolute calibration : use of the refined sun-diffuser BRDF
Trends of time evolution are much more similar for the different bands
    Slight oscillations (low frequency) but a more apparent sensitivity loss with time for VNIR bands
Temporal evolution of absolute gains for SWIR bands becomes smoother
Operationally applied since 2017 October 23rd
(older products will be reprocessed)
Changes for the first acquisition (ref)

## Slide 9: S2A spectral bands
Errors during the on-ground characterization for S2A spectral bands :
  Spectral responses are being recalculated
  B02 and B01 bands mainly impacted
CNES results:
Conversion of the Rayleigh method result for the B02 band by using the S2B spectral band definition rather than the S2A
Single test not significative to conclude the S2A band shape must be replaced by the S2B
Cross-check with other vicarious methods is necessary
CNES courtesy
Spectral response for band B02 (490 nm)
Spectral response for band B01 (443 nm)

## Slide 10: S2 Radiometric validation
Validation by vicarious calibration methods
  Absolute calibration method: Rayleigh signal over ocean / simulation
  Interband calibration method: Sun-glint signal over ocean (not applied)  geometric design avoid the sun-glint
  Desert (PICS) calibration: Comparison TOA reflectance / simulation
  Inter-sensor calibration method: Comparison TOA reflectance of sensors

## Slide 11: S2 Radiometric validation
Focus on Rayleigh calibration results over S2A
Vicarious CalVal Ocean sites (yellow)
TOA observation
Average value : 0.1° x 0.1°
Aerosol filtering (NIR threshold)
Simulation
Solar irradiance : Thuiller 2003
Water leaving radiance : Morel and Maritorena (2001)
LibRadtran code

## Slide 12: S2 Radiometric validation
Focus on Rayleigh calibration results over S2B
  Preliminary results
    over 4 months
    8 acquisitions
Vicarious CalVal Ocean sites (yellow)

## Slide 13: S2 Radiometric validation
Desert sites calibration over 6 CEOS-PICS: Sub-region used for S2A, S2B and LANDSAT
Algeria-5
Algeria-3
Libya-1
Libya-4
Mauritania-1
Mauritania-2

## Slide 14: S2 Radiometric validation
Focus on desert sites calibration over S2A & S2B
Bouvet 2014 method:
BOA BRDF built from MERIS data
Simulation of the TOA observation for
- MSI acquisition geometry
- Ozone and WV content from ECMWF
- Constant AOT

## Slide 15: S2 Radiometric validation
Focus on Sensor-to-Sensor TOA reflectance comparison over S2A & S2B & LS8
Chart: Wavelength (nm)
| 443 | 490 | 560 | 665 | 865 | 1610 | 2190
Avg-All | 1.0352 | 1.0376 | 0.99874 | 1.0412 | 1.015 | 1.0172 | 1.015
Alg3 | 1.0153 | 1.0255 | 0.98772 | 1.0344 | 1.0093 | 1.0068 | 0.99469
Alg5 | 1.0137 | 1.0191 | 0.99317 | 1.0507 | 1.0186 | 1.0264 | 1.0173
Lib1 | 1.0205 | 1.0383 | 0.99115 | 1.0326 | 1.0085 | 1.0077 | 0.9921
Lib4 | 1.0556 | 1.0603 | 1.0134 | 1.0421 | 1.0124 | 1.0119 | 1.0136
RRV | 1.0508 | 1.0367 | 1.0189 | 1.0458 | 1.0305 | 1.039 | 1.0436
MAU1 | 1.0465 | 1.0422 | 0.99112 | 1.0323 | 1.0034 | 1.0044 | 1.0151
MAU2 | 1.0441 | 1.0412 | 0.99577 | 1.0503 | 1.0228 | 1.0238 | 1.0284
Chart: Wavelength (nm)
| 443 | 490 | 560 | 665 | 705 | 740 | 783 | 842 | 865 | 945 | 1370 | 1610 | 2190
Avg-All | 0.98862 | 0.99437 | 0.99156 | 0.99738 | 0.99126 | 0.98337 | 0.98624 | 0.99757 | 0.99016 | 0.99228 | 1.0241
Alg3 | 0.98298 | 0.99116 | 0.99036 | 0.99779 | 0.98966 | 0.98179 | 0.98586 | 0.99439 | 0.98993 | 0.98806 | 1.025
Alg5 | 0.98826 | 0.99804 | 0.99685 | 1.0019 | 0.99623 | 0.98961 | 0.9904 | 1.0049 | 0.99306 | 0.99043 | 1.0173
Lib1 | 0.99814 | 1.0012 | 0.99232 | 1.0026 | 0.98917 | 0.98328 | 0.9853 | 0.99548 | 0.98938 | 0.99565 | 1.0286
Lib4 | 0.98713 | 0.98906 | 0.98457 | 0.99045 | 0.98312 | 0.97311 | 0.98152 | 0.99003 | 0.98706 | 0.99466 | 1.01
RRV | 0.9866 | 0.99236 | 0.99372 | 0.9941 | 0.99811 | 0.98906 | 0.98812 | 1.0031 | 0.99138 | 0.99262 | 1.0398
S2A/LS8 N#: 63
S2B/S2A N#: 43
Results without any processing (only selection criteria)
Consistency in a range of 5% depending on the site
MSI-A reflectance > OLI reflectance
Consistency in a range of 2% depending on the site
MSI-A reflectance > MSI-B reflectance by ~ 1%

## Slide 16: S2 Radiometric validation
Focus on In-situ measurements: 23 overpasses are provided by NASA via ESA
RRV site: S2A/MSI-L1C (Tile : T11SPC)
23/08/2015
Chart: Sentinel-2A MSI Band
| B01 | B02 | B03 | B04 | B05 | B06 | B07 | B08 | B8A | B09 | B10 | B11 | B12
MPC | 0.99783 | 0.99483 | 1.0042 | 1.0285 | 1.0175 | 1.0089 | 1.0133 | 0.99981 | 1.01 | 0.94853 | 1.0176 | 0.99613
/
Average value 1 x 1 km2
Simulation from University of Arizona
945 nm
(water vapor)

## Slide 17: S2 Radiometric validation
Overall methods results
  Discrepancies between methods < 5%
  MSI reflectance > OLI reflectance
  MSI-B reflectance < MSI-A reflectance (~1%)
S2A
S2B

## Slide 18: S2 inter-sensors comparison
Focus on PICS method: S2A, S2B, LS8 inter-comparison
MSI-A reflectance > MSI-B reflectance
Some coincident validation points match quite well between MSI-A & OLI at 865 nm

## Slide 19: S2 inter-sensors comparison
Focus on PICS method: S2A, S2B, LS8 inter-comparison
  Same spectral shapes of calibration results for MSI-A & MSI-B (except B02 band : Spectral response impact is under investigation)
  Good consistency in a range of 1-2% between OLI & MSI (except for B01 band)
Chart: Wavelength (nm)
| 443 | 490 | 560 | 665 | 705 | 740 | 784 | 842 | 865
MSI_A | 0.98826 | 0.98136 | 1.0091 | 1.003 | 1.0131 | 1.0047 | 0.98727 | 0.99952
MSI_B | 0.97731 | 0.97842 | 0.98547 | 0.98517 | 0.9935 | 0.98932 | 0.97143 | 0.99077
OLI | 0.95808 | 0.98429 | 0.99389 | 1.0052 | 0.99116 | 0.99116

## Slide 20: To conclude
Summary
  Absolute gains are stable (VNIR bands) and properly monitored by sun-diffuser acquisitions
  Validation activities check operational calibrations
    A shift by about 1% is measured between most of S2A / S2B bands
    A good calibration agreement of TOA reflectance between S2 & L8 (1-2%)
  A refinement of S2A spectral characterization is in progress
    How to improve calibration approaches for a better data interoperability of S2 & L8 ?
  Confirm we compute calibrations with the same solar irradiance model and Earth-Sun distance
  Perform vicarious calibrations over same sites, using same spectral characterization of the targets, same atmospherical parameters (same RT code), quasi-simultaneous observations
Thank you for your attention!